## Slide 1: Moller Polarimetry Update Don Jones Temple University
Dec. 2021
MOLLER Collaboration Meeting

## Slide 2: CREX results
Agreement with Compton at +/-0.02% level
0.2%
0.5%

## Slide 3: CREX results
Record accuracy for JLab Moller polarimetry
Particular progress made on Azz systematic
It looks like we will be able to reach 0.14% or better uncertainty for Azz at 11 GeV.
--------------
0.14
0.30
0.05
0.04
0.01
0.05
0.06
0.10
0.20
0.00
0.00
--------------
0.41
--------------
Wanted

## Slide 4: Moller Azz: two recent improvements
Our knowledge of spectrometer optics (field maps) is limited to several percent uncertainty, BUT simulation shows if we calibrate our settings relative to the rate maximum, we are highly insensitive to absolute knowledge of optics.
Limiting the vertical detector acceptance allows AND overtuning past rate peak to pull electrons off dipole walls allowed us to tune the Levchuk correction to nearly 0 AND create a large flat region of Azz.
PREX 8 PMT simulation
1.3%
Simulated Azz
Levchuk Corr Azz
Coincidence Rate
PREX 2 PMT simulation
Simulated Azz
Levchuk Corr Azz
Coincidence Rate
Quadrupole 1 Tune
Quadrupole 1 Tune
Caveat: results for 4.5cm vertical detector acceptance.
May require detector redesign or collimator.

## Slide 5: Azz at 11 GeV optics
Coincidence Rate
Simulated Azz
Levchuk Corr Azz
At 11 GeV with current optics we are unable to tune away significant Levchuk correction nor create a flat region insensitive to accurate knowledge of the optical tune
Moving target 30 cm upstream accomplishes what we want and is now officially implemented in beam line design.

## Slide 6: Beam line redesign being implemented
Moving Moller target coils upstream required some re-configuring of the beam line design: design changes now included in model
Plan in place to implement improved MOLLER beam line including Moller target move before MOLLER
  Could be as early as Spring 2022, although the probability for getting all parts in hand on time is low
  Early implementation gives us time to study impact of redesign and benchmark simulation ahead of time

## Slide 7: Another recent improvement for Azz
Levchuk correction requires a model of the momentum distributions for polarized and unpolarized electrons in Fe
For past two decades this correction has been done using distributions from modified hydrogen wavefunctions
Data from CREX showed that this calculation predicted a 30% smaller “peak” than measured
Reached out to expert John Perdew* at Temple University and his student Aaron Kaplan suggested a Hartree-Fock model and provided the momentum distributions.
Exciting agreement!
*John Perdew is one of the most highly cited scientists of all time with over 150,000 Google citations

## Slide 8: CREX results
Systematics inflated by foil polarization and high current extrapolation
These two contribute a total of 0.76% and the rest is 0.38%
Likely overestimated (given level of agreement with Compton which had 0.5% uncertainty) but difficult to limit without better measurements
--------------
0.14
0.30
0.05
0.04
0.01
0.05
0.06
0.10
0.20
0.00
0.00
--------------
0.41
--------------
Wanted

## Slide 9: Extrapolation to High Current
Potential to be the limiting systematic unless we measure it.
We will develop a plan to directly measure:
  Beat frequency method used before where the laser is tuned just off the 499 MHz so only every nth pulse actually goes to the hall but full power on photocathode.
  Can investigate what statistics Compton could get at 5 uA for 8 hrs.

## Slide 10: Foil polarization
Potentially large systematic: 1% smaller polarization during PREX-2 when running on a wrinkle
Attempts to measure with Kerr apparatus only partially successful.
Kerr apparatus: modulate polarization at fixed frequency and pull out polarization signal on reflected light from magnetized foil with lock-in amplifier (magnetization rotates polarization)
Publication nearly ready to submit to NIM that shows Fe foil polarization at saturation known to ±0.24%
Still need to prove that we are at saturation
Sensitivity of degree of saturation on foil and angle and flatness needs to be measured

## Slide 11: Kerr apparatus
Example saturation curves taken with Kerr apparatus
Not able to conclusively reach saturation, but see signature of interference effects
Longer careful study required but may not be possible.
Need to develop plan for using beam to set upper limit on this systematic

## Slide 12: GEMs for Moller polarimeter
GEMs are being installed between the dipole and the detector to help verify simulated radiative, Levchuk and multiple scattering effects.
Design recently completed by Nilanga’s group at UVA -- ready for construction
Readout split into right and left required to allow for resolution of left and right coincident Moller electrons
Support structure design to start soon

## Slide 13: Collimator
Addition of a collimator is part of the project to help limit systematics
Need more simulation work to decide if this is needed and what its design should be
May be required to limit vertical acceptance on detector (remove sensitivity to Levchuk and knowledge of quad optics settings)
Target date set to make design decision by early April

## Slide 14: Active personnel
Temple University: D. Jones, J. Napolitano, and recently Eric King working on a variety of systematic and design issues
Syracuse University: P. Souder and student Faraz Chahili working on insights from future GEMs and how they can be used to verify the simulation inputs
Jefferson Lab: Simona, Dave Gaskell, and Bill Henry maintain and upgrade hardware/software
University of Virginia: Kent Paschke maintains critical eye and provides key advice/insight.

## Slide 15: Summary
Encouraging progress made on systematics during PREX-2 and CREX
Progress on Azz+Levchuk systematics nearly meet MOLLER requirements
Two systematics (foil polarization and high current extrapolation) are highest priorities and will likely require beam time to limit
Progress is being made on hardware improvements included in the MOLLER project, with
  GEM design complete and support structure design to begin soon
  Collimator design choice made by early Spring.
All systematics being reviewed carefully